## Slide 1: QUIC performance
QUIC and Satellite
Open Stakeholder Meeting
Lorena Albiol, Indra Sistemas, lalbiol@indra.es
04/11/2020

## Slide 2: Performance Evaluation Test bed – Fixed BW (1)
TCP client (curl)
QUIC client
PEP
(satellite side)
Satellite network
emulator (AINE)
PEP
(ground-side)
TCP server (Apache)
QUIC server
SATELLITE
GROUND
RTT = 650 ms
2M (RTN)
10M (FWD)
Fixed BW
Downloaded file
  100kB
  1MB
  2MB
  10MB
  100MB

## Slide 3: Performance Evaluation Test bed – BoD (1)
TCP client (curl)
QUIC client
PEP
(satellite side)
Satellite network
emulator (AINE)
PEP
(ground-side)
Terr Delay Emul
(10 ms)
TCP server (Apache)
QUIC server
SATELLITE
GROUND
RTN link with
Bandwidth On Demand
20k CRA, 2M VBDC
2M (RTN)
10M (FWD)
Average RTT = 625 ms
Downloaded file
  100kB
  1MB
  2MB
  10MB
  100MB

## Slide 4: QUIC Performance with a short file transfer
QUIC
TCP
TCP & PEPs
Effects of connection set-up and initial congestion window
quicly, March 2020, IETF draft-27
https://github.com/uoaerg/quicly

## Slide 5: QUIC Performance with a short file transfer
QUIC supports 1-RTT connection set-up
But initial QUIC packet is larger. This is noticeable with BoD.
QUIC/quicly performance similar to TCP NewReno with TLSv1.3
QUIC
TCP
QUIC
TCP
quicly, March 2020, IETF draft-27
https://github.com/uoaerg/quicly

## Slide 6
Much better performance with PEPs (Fast Start, high IW).
TCP & PEPs
TCP & PEPs
QUIC Performance with a short file transfer
QUIC
TCP
quicly, March 2020, IETF draft-27
https://github.com/uoaerg/quicly

## Slide 7: QUIC Performance with a medium file transfer
Performance with PEPs is still much better
TCP & PEPs
QUIC
TCP
quicly, March 2020, IETF draft-27
https://github.com/uoaerg/quicly

## Slide 8: QUIC Performance with a long file transfer
Performance differences with /without PEPs become less relevant.
Data rate becomes main performance driver.
quicly, March 2020, IETF draft-27
https://github.com/uoaerg/quicly

## Slide 9: Performance tests with Chromium IETF QUIC
Better performance of Chromium QUIC
IW = 32 instead of IW = 10
QUIC - quicly
QUIC - Chromium
QUIC - quicly
QUIC - Chromium
Chromium QUIC, IETF draft-29, retrieved 3/06/2020 (https://www.chromium.org/quic/playing-with-quic)

## Slide 10: Performance tests with Chromium IETF QUIC
QUIC - quicly
QUIC - Chromium
Performance problems of Chromium QUIC implementation with BoD
  Hybrid Fast Start feature
  Does not work well with more variable RTT of BoD scenario
    Premature entry into congestion avoidance
Chromium QUIC, IETF draft-29, retrieved 3/06/2020 (https://www.chromium.org/quic/playing-with-quic)

## Slide 11: Performance Evaluation Test bed – Fixed BW (2)
TCP client (curl)
QUIC client
PEP
(satellite side)
Satellite network
emulator (AINE)
PEP
(ground-side)
TCP server (Apache)
QUIC server
SATELLITE
GROUND
RTT = 650 ms
10M (RTN)
50M (FWD)
Fixed BW
Downloaded file
  100kB
  1MB
  2MB
  10MB
  100MB

## Slide 12: Performance Evaluation Test bed – BoD (2)
TCP client (curl)
QUIC client
PEP
(satellite side)
Satellite network
emulator (AINE)
PEP
(ground-side)
Terr Delay Emul
(10 ms)
TCP server (Apache)
QUIC server
SATELLITE
GROUND
RTN link with
Bandwidth On Demand
20k CRA, 10M VBDC
10M (RTN)
50M (FWD)
Average RTT = 625 ms
Downloaded file
  100kB
  1MB
  2MB
  10MB
  100MB

## Slide 13: QUIC Performance – 50M/10M scenario
Similar considerations as for the Small scenario
Effects of higher bandwidth become more relevant for ≥ 10MB
Flow control disabled (QUIC) or tuned parameters (TCP)

## Slide 14: QUIC performance conclusions
QUIC performance similar to TCP / NewReno (with connection start-up improvements)
Scenarios with PEPs provide much better performance for short to medium file sizes
  Typical of web browsing
Non-standard QUIC congestion control features may need to be tuned for satellite (Hybrid Fast Start)
  QUIC provides increased flexibility to optimize congestion control
  May be dangerous for scenarios that are not the main target
Impact of QUIC flow control on performance >> for further study