## Slide 1
QUIC and Satellite Open Stakeholder Meeting
Accelerating Start-up
Nicolas KUHN
nicolas.kuhn@cnes.fr

## Slide 2: Typical GEO satellite-based Internet access
Solution #1 : adapt the end-to-end protocols
Solution #2 : inform end point of the path characteristics
Local Access Network
Satellite Access Network
Satellite ISP Network
« Internet »
QUIC and Satellite Open Stakeholder Meeting - Accelerating Start-up
Data rate | High | High | Variable | Average
Latency | Low | Low | High | Low
Loss | No loss | Congestion losses | No loss | Loss if Wi-Fi

## Slide 3: Solution #1 : adapt the end-to-end protocols
Multiple paths with split
End-to-end path without split
QUIC and Satellite Open Stakeholder Meeting - Accelerating Start-up
Utilised platform for tests
QUIC SERVER
QUIC CLIENT
Delay / capacity limitation
Losses
IPERF3 SERVER
IPERF3 CLIENT
PEPSal
PEPSal
Delay / capacity limitation
Losses
picoquic/picoquic (h3-25/24/23)
or
h2o/quicly(h3-25)
picoquic/picoquic (h3-25/24/23)
or
curl/ngtcp2 (h3-25)
Default
Kernel 4.15
Ubuntu 16.04
iperf3 v3.6
Default
Kernel 4.15
Ubuntu 16.04
iperf3 v3.6
Default ; Kernel 4.4
Same configuration on both PEP client and PEP server
 | TCP_WMEM_MAX (MB) | TCP_RMEM_MAX (MB) | CORE_WMEM_MAX CORE_RMEM_MAX (MB) | ICWND IRWND (packets)
NO PEP | 4 | 6 | 0,2 | 10
PEP A | 4 | 6 | 0,2 | 10
PEP B | 4 | 6 | 0,2 | 100
PEP C | 33 | 33 | 33 | 10
PEP D | 33 | 33 | 33 | 100

## Slide 4: Solution #1 : adapt the end-to-end protocols
Focus on the 50 Mbps / 10 Mbps use-case
Multiple paths with split
QUIC and Satellite Open Stakeholder Meeting - Accelerating Start-up
With TCP-Proxy:
  Capacity to reach channel capacity
  Reduced transmission time
Proposed objectives :
  2MB: 3 sec
  10 MB: 5 sec
  100MB: 20 sec

## Slide 5: Solution #1 : adapt the end-to-end protocols
Focus on the 50 Mbps / 10 Mbps use-case
End-to-end path without split
QUIC and Satellite Open Stakeholder Meeting - Accelerating Start-up
CURL CLIENT
PICO-QUIC CLIENT
PICO-QUIC (Version v0.24d) client
  PICO-QUIC server (Version v0.24d) : the objectives are met
  H20 server (2.3.0-DEV@9f65c27) : the objectives are not met
CURL client (Version 7.69.0-DEV (x86_64-pc-linux-gnu) libcurl/7.69.0-DEV OpenSSL/1.1.1d zlib/1.2.8 brotli/1.0.4 ngtcp2/0.1.0-DEV nghttp3/0.1.0-DEV)(any server)
  The objectives are not met

## Slide 6: Solution #1 : adapt the end-to-end protocols
Designing a CC that is relevant for all deployment cases may not be relevant
Knowing about the path characteristics can help in adapting the CC in specific deployment scenarios
  Tuning RTT_INIT
  Tuning flow control parameters (MAX_STREAM_DATA)
Issue in CC convergence in SATCOM use cases
QUIC and Satellite Open Stakeholder Meeting - Accelerating Start-up

## Slide 7: Solution #2 : inform end point of the path characteristics
QUIC and Satellite Open Stakeholder Meeting - Accelerating Start-up
The objective: inform end point of the path characteristics
    Based on previous connections
    During a connection:
      Both peers measure BDP (rtt * bytes_in_flight)
      The server sends to the client the information that has been measured
    When reconnecting:
      Client sends a 0-RTT token for faster connection establishment
      The idea: add the information from previous BDP to the server
See draft-kuhn-quic-0rtt-bdp-07 for how it could be done in QUIC
  There is also a strawman algorithm in the draft on how to safely jump to the available capacity
  The results showed here :
    No safe jump
    The server uses directly previously measured BDP

## Slide 8: Solution #2 : inform end point of the path characteristics
End-to-end path without split
QUIC and Satellite Open Stakeholder Meeting - Accelerating Start-up
Focus on the 50 Mbps / 10 Mbps use-case
Time needed to download 10 MB
0-RTT-BDP
0-RTT
No 0-RTT
Cumulative Density Function
Cumulative Density Function
Cumulative Density Function

## Slide 9: Solution #2 : inform end point of the path characteristics
End-to-end path without split
QUIC and Satellite Open Stakeholder Meeting - Accelerating Start-up
Focus on the 250 Mbps / 3 Mbps use-case
Time needed to download 10 MB
0-RTT-BDP
0-RTT
No 0-RTT
Cumulative Density Function
Cumulative Density Function
Cumulative Density Function

## Slide 10: Summary
QUIC and Satellite Open Stakeholder Meeting - Accelerating Start-up
We are working at IETF on this
  If you are interested, please join the ETOSAT list: https://www.ietf.org/mailman/listinfo/Etosat
  Or discuss our drafts
    draft-kuhn-quic-0rtt-bdp-07
    draft-kuhn-quic-4-sat-06
On the median case
  0-RTT-BDP improves by approx. 25% cases with no 0-RTT
  0-RTT-BDP improves by approx. 10% cases with *just* 0-RTT
The CC has been simply modified
  More specific optimization could be imagined
What is going on ?
  What are the impacts of RRM mechanisms or various satellite-based (variable delay in mega constellation, etc.) or losses, etc on the end-to-end performance of QUIC ?
  What are the performance of application level designs ? Do they need specific tuning or implementations ?